SOF Riverine and Combatant Craft Operations Facility
# Stennis Space Center, MS
# Site/Civil/Architectural Basis of Design – 50% Submittal 12/8/08

# The Site Plan and Building Design have evolved through the design process including PAK and CDW meetings to simultaneously better suit User needs and more closely conform to the RFP.
# Site Plan

Note: SWPPP has been submitted and has received a satisfactory review.

Traffic flow to the site has been studied with various options explored:

POV access is now from Lower Gainesville Road.
- POV parking and future parking has been redesigned.
# “LEED” preferred parking is indicated.
# Construction access points have been proposed.
# Construction activity areas have been defined.
# Site clearing limits have been adjusted to minimize impact.
# Landscaping locations have been refined to enhance security and provide ease of maintenance.
# Standoffs have been maintained and specifically improved at vehicle entrance.
# Parking for oversized government vehicles has been provided.
# User input has helped refine daily personnel flow:
# - Preferred facility views, both outward and approaching the site have been established.
# - Foot traffic from parking and between buildings has been better accommodated.
# - Pad locations for antenna, chiller, condensers, transformers, and generator are proposed.

# Land Structures

Operations & Maintenance Building

# Overall dimensions have not changed, but interior layout dimensions have been fine tuned to better suit User needs and conform to good construction practice. Major elements of floor plan flow have been changed to suit input from Users:
# Exterior “Sailor” entrance to the Operations Facility from parking and boat storage functions is now centralized for convenience of access to Cages, Staging, or Operations. Vertical circulation has moved across the building to coincide with the “Sailor” entrance.
# Exterior “formal” entrance has been defined to coincide with preferred approach from the site vehicle access point.
# Entrance canopy at “formal” entrance has been extended to enhance weather protection and become a stronger visual element.
# Clerestory windows have been moved from the Operations area of the building to the Staging area of the building to conform with the RFP.

Interior function of the facility continues to be refined:

- User has updated Armory layout, specifically cage arrangement and room furnishings.
- Toilet rooms and shower facilities have been refined based on User input.
- Design staff has met on site to further define all office and furniture layout.

Boat Storage Building

Ongoing discussions with the User are resulting in further detailing of the design of the critical raised platforms to access the boats:

- Concrete versus steel.
- Mesh partitions.
- Personnel entrances.