ENCE 3341
SOIL MECHANICS LAB
LAB 4
STANDARD PROCTOR
COMPACTION TEST

Brandon Nowakowski

Introduction:
It is often necessary improve the strength of soil used for the foundations of buildings, roads, and other structures. The Proctor test is used to determine the dry unit weight and optimum moisture content of soil for field compaction. The test is design for soil passing the US No.4 sieve.

Equipment List:
1. Compaction mold
2. US No.4 Sieve
3. Standard Proctor hammer of weight 5.5lb
4. Balance sensitive to 0.1lb
5. Balance sensitive to 0.01g
6. Large plastic pan
7. Jack
8. Spatula
9. Moisture cans
10. Oven

Procedure:
1. Acquire 2400g of air dry soil.
2. Weigh the empty mold, and empty moisture cans without lid.
3. Add distilled water to the soil to achieve about 8% moisture content. (approx 192g water)
4. Mix the soil and then add 1/3 mold full. Perform 25 blows with the Proctor hammer in a circular fashion. Add another 1/3 mold full. Perform 25 more blows. Finally add another 1/3 mold full and compact with hammer.
5. Remove the mold cap and level the soil off with a spatula.
6. Weight the mold + moist soil.
7. Use the jack to remove the soil. Place a portion of the soil in a moisture can and put it in the oven for 24 hours.
8. Repeat steps 3-7 for moisture content 12% and 16%.

Calculations:
Moist Unit Weight = %gamma_m = {W_2-W_1} over {1/30}
Moisture Content = w={M_4-M_5} over {M_5-M_3} (100)
Dry Unit Weight = %gamma_d={%gamma_m} over {1+(w/100)}
Zero Air Void Unit Weight = %gamma_z={%gamma_water} over {(w/100)+(1/G_s)}

Conclusion:

The soil sample was found to have a maximum dry unit weight of approx 107lbs/ft2, and an optimum moisture content of 14% as shown in the following graphs and charts.