Sieve Analysis

January 27, 2011

David Dammon

Introduction/Purpose: To determine the particle sizes in a given soil sample and draw particle size distribution curve.

List of Equipment

- Set of ASTM sieves: Cover, #4, #10, #20, #50, #60, #80, #140, #200, Bottom Pan
- Electrical balance
- Mechanical Sieve Shaker
- China dish

Procedure:
a. First, a sample of soil (506.4 g) was poured into a set of ASTM sieves (Cover, #4, #10, #20, #50, #60, #80, #140, #200, Bottom Pan) which was then put into a mechanical sieve-shaker.

b. The soil remained in the mechanical sieve-shaker for 15 minutes and then the shaker was turned off. The eight sieves and the bottom pan were then removed from the shaker.

c. Starting with the top sieve, #4, the soil was poured into the china dish and then measured using an electrical balance, (the mass of the china dish was subtracted from the measurement then logged). The remaining 7 sieves and bottom pan were measured in the same manner.

Results:

Particle Size Distribution
Particle Size (mm)
Percent finer
5. Conclusion/discussion: According to the results of the Grain-Size Distribution Curve, I can conclude that the sample tested in class is a well graded soil. A well graded soil is a soil whose particle sizes are distributed over a wide range. The total mass of the soil analyzed was 506.4 g, however at the end of the experiment the soil measured from all of the compartments of the ASTM sieves only added up to 504.9 g. The 1.5 g of soil was lost during the experiment due to either sticking to the sides of the sieves or falling out of the sieves during the measurement. This concludes that the experiment was 99.7% accurate representation of the tested soil.