Particle Size Distribution
Particle Size (mm)
Percent Finer

Hydrometer Analysis

February 3, 2011

David Dammon

Introduction/Purpose: To determine the particle sizes in a given soil sample and draw particle size distribution curve.

List of Equipment
- ASTM 152-H Hydrometer
- Mixer
- Two 1000 cm3 graduated cylinders
- Thermometer
- Defloculating Agent (4%) Sodium Heametaphosphete
- Spatula
- Beeker
- Balance
- Distilled water
- #13 Rubber Stopper
- Plastic Squeeze bottle
- 50 grams of oven dried soil with a Specific Gravity (Gs) of 2.65

Procedure:
a. A sample of soil (50 g) was supplied. Deflocculating Agent (4% solution) was prepared and 125 cc's of this deflocculating agent was added to the soil. This solution was allowed to soak for 8 – 12 hours.
b. 875 cc's of distilled water was added to the first 1000 cm3 graduated cylinder, then 125 cc's of the deflocculating agent was added. This solution was then mixed.

c. A control measurement was taken to obtain a zero reference and meniscus correction using the hydrometer in the first cylinder. This measurement entailed taking the temperature and reading the ASTM 152-H hydrometer in the solution at the top fluid mark of the hydrometer and the actual level of the fluid in the first cylinder, then recording the readings.

d. The soil and solution, from item a above, was then mixed using a spatula and poured into a second 1000 cm3 graduated cylinder, then entire contents of the soil and solution were moved into the second cylinder by using a plastic squeeze bottle filled with distilled water. Additional distilled water was then added to the second cylinder to top the level at the 1000-cc mark, it was then capped with a rubber stopper. This second cylinder was then mixed by turning the contents upside down and back for approximately 1 minute.

d. Measurements were then taken at 0, 2, 5, 8, 15, 30, 60, 120, 929, 1152, and 1332 minutes after mixing the solution. Each measurement entailed inserting a thermometer and ASTM 152-H hydrometer into the cylinder containing the soil-water suspension, then recording the readings. After each reading the hydrometer was removed from the soil-water suspension and returned to the control cylinder. The thermometer was removed and placed in the storage case.

Results:
Conclusion/discussion: According to the results of the Hydrometer Analysis, I can conclude that this sample tested in class is a silty-clay mixture and that this sample was not from the original soil sample performed in LAB #1 because of the disjointed graph above.