Liquid Limit and Plastic Limit

February 10, 2011

David Dammon

Introduction/Purpose: Atterberg Limits Determination (ASTM D4318). To determine the Liquid Limit and the Plastic Limit of a given soil sample.

List of Equipment

- Casagrande's Liquid Limit device
- Grooving Tool
- 4ea. Moisture Content Cans
- 2ea. Porcelain evaporating dish
- Spatula
- Electronic Balance
- Plastic Squeeze Bottle
- Oven
- Grounded Glass Plate
Procedure:
a. First, a sample of air dry soil (250g) was separated for the two test, approximately 20g was poured into a separate porcelain evaporating dish for the second portion of this test. The remaining 200g of soil was mixed with water until the sample was pliable. All of 4 of the Moisture Content Cans were measured for their empty mass and these measurements were recorded below.

b. A portion of the pliable soil was placed in the Casagrande's LL device and a groove was then cut into the soil using the Grooving Tool. The Casagrande device was then cranked a number of times to determine how many blows it took to move the separated sides together, the number of blows were then recorded. The portion of pliable soil in the Casagrande device was then placed one of the Moisture Content can and measured for mass, then the mass was recorded below. A little more water was added to the soil sample, two time, and the same procedure above was completed. This gave a count of 3 times the soil was tested, with different amounts of water. After completing all three tests above, the soil sitting in 3 of the 4 Moisture Content cans were placed in the oven.

c. The separated portion of air dry soil (20g) was then mixed with water to test the plastic limit. Once the correct pliable mixture was obtained, small portions of the sample were placed on the Ground Glass Plate, approximately 1/8” in diameter. These sub-samples were rolled using the palm of the hand until the sub-samples started to crumble.

Results from the Liquid Limit test:

Liquid Limit Test
Number of Blows
Moisture Content (%)

5. Conclusion/discussion: According to the results of the Liquid Limit and Plastic Limit tests the soil tested would be a clay mineral Kaolinite.