Standard Proctor Compaction Test

February 17, 2011

David Dammon

Introduction/Purpose: This test is to determine the optimum moisture content of a soil that will enable a contract to properly compact a given soil.

List of Equipment

- Compact Mold with a 4” diameter, 4.584” in height, with a volume of 1/30 ft3 = 943 cm3
- Hammer 5.5# with a fall height of 12”
- Large flat pan
- Jack
- Electronic Balance
- Plastic Squeeze Bottle
- Oven
- Steel straight edge
- 4 moisture cans
Procedure:
a. Weigh and document the empty mold, empty moisture cans without lid.

b. A sample of air dry soil 2400g was provided in a large flat pan. 192 ml of water was added and throughly mixed with the soil sample to achieve an assumed moisture content of 8%.

c. A quantity of soil was placed in the compact mold in 3 lifts, each lift was compacted with a 5.5# hammer. The mold with the moist soil was weighed and a small sample was placed in an empty moisture can.

d. The remaining soil from the compact mold was replaced in the large flat pan. Then three additional tests were performed by adding water to achieve an assumed moisture content of 12%, 16%, 20%. The tasks in item c above were performed for each test.

e. After completing all four tests above, the soil sitting in the 4 Moisture Content cans were placed in the oven. The next morning after completely drying the dry soil and moisture content cans were measured.

Calculations:
Moist Unit Weight = %gamma_m = {W_2-W_1} over {1/30}
Moisture Content = w={M_4-M_5} over {M_5-M_3} (100)
Dry Unit Weight = %gamma_d={%gamma_m} over {1+(w/100)}
Zero Air Void Unit Weight = %gamma_z={%gamma_water} over {(w/100)+(1/G_s)}

Results from the Standard Proctor test:

Moisture Density Curve
Moisture Conctent w,(%)
Dry Unit Weight, lb/ft3

6. Conclusion/discussion: The optimum moisture content for compacting this soil is 15% and γd max is 105 lbs/ft3.