Chapter 2
Uniformity Coeff.	Coeff. Of gradation

Hydrometer Analysis

Liquid Limit is where the number of blows = 25, read on the curve the moisture content.
Plastic Limit is
PI = LL – PL

Dry Unit Weight: %gamma_d = {W_s} over {V} = {G_s(%gamma_water)} over {1 + e} Degree of Saturation: S = {V_w} over {V_v} Moisture Content: w = {W_w} over {W_s}

Void Ratio: e = {G_s(%gamma_water)} over {%gamma_d} - 1 Relative Density: D_r = {e_max-e} over {e_max-e_min}
e = in situ void ration of the soil
emax = void ratio of the soil in the loosest state
emin = void ratio of the soil in the densest state

(US) Moisture content w = Wwater/Wsolid soil Ww = Wns -Wd
Moist unit weight γ = W/V γd = Ws/V	γw = 62.4#/ft3
Degree of saturation Se = wGs
Porosity γd = Gs γw (1-n) Solve for n

(Metric) Dry density
Porosity n = e/(1+e)
Degree of Saturation %
Mass of water in kg/m3

Chapter 6 Soil Compaction
Standard Proctor Compaction test:
Volume (mold) Wt.of wet soil Moisture content Moist Unit weight of compaction Dry Unit weight ZAV weight
       1/30 W w %gamma = {W} over {V_m} %gamma_d = {%gamma} over {1 + ({w} over {100}) }
Zero Air Voids:
Moisture Content ZAV Unit weight
        w %gamma_zav = {%gamma_w} over {w+({1} over {G_s}) }

Relative Compaction R = γd / γd(max) [from curve] x 100
Dry density γd (field)

Relative Compaction Percent: R = {%gamma_dfield} over {%gamma_maxlab}*100 where %gamma_dfield = {%gamma_moist} over {1 + ({w} over {100}) }

Vibroflotation Device: Vibroflotation given D10, D20 and D50; When Sn 10 – 20 (good)

Suitability No.: S_n = 1.7*sqrt{{3} over {D_50^2}+{1} over {D_20^2}+{1} over {D_10^2} }

Chapter 7 Permeability

Total head: h = {u} over {%gamma_w} + Z where Z=hydraulic head, u=pressure Head loss: i = {%DELTA h} over {L} where i=hydraulic gradient

Darcy's Law: v = ki where v=discharge velocity, k=hydraulic conductivity

Hydraulic Conductivity: k = {%gamma_w} over {%eta}* K where ή=viscosity of water, K=absolute permeability

Constant Head Test:
    k = {QL} over {Aht} v = ki

Equivalent Hydraulic Conductivity:

k_Heq = {1} over {H} * (k_H1*H_1 + k_H2*H_2 + k_H3*H_3) k_Veq = {H} over {({H_1} over {k_V1} + {H_2} over {k_V2} + {H_3} over {k_V3}) } Equiv. Hyd. conductivity: {k_Heq} over {k_Veq}

Moisture Density Curve

Volume cm3	Volume m3	Mass of wet soil	γ	Moisture Content	γd
943.3	0	1.68
	X 10 -6		W/V		γ/(1+w/100)