Chapter 2
Uniformity Coeff.	Coeff. Of gradation

Hydrometer Analysis

Liquid Limit is where the number of blows = 25, read on the curve the moisture content.
Plastic Limit is
PI = LL – PL

Relative Density
Dr = relative density,
e = in situ void ration of the soil
emax = void ratio of the soil in the loosest state
emin = void ratio of the soil in the densest state

(US) Moisture content w = Wwater/Wsolid soil Ww = Wns -Wd
Moist unit weight γ = W/V γd = Ws/V	γw = 62.4#/ft3
Degree of saturation Se = wGs
Porosity γd = Gs γw (1-n) Solve for n

(Metric) Dry density
Porosity n = e/(1+e)
Degree of Saturation %
Mass of water in kg/m3

Moisture Density Curve

Volume cm3	Volume m3	Mass of wet soil	γ	Moisture Content	γd
943.3	0	1.68
	X 10 -6		W/V		γ/(1+w/100)

Relative Compaction R = γd / γd(max) [from curve] x 100

Dry density γd (field)
Percent Relative Compaction

Vibroflotation given D10, D20 and D50; When Sn 10 – 20 (good)