Design Wind Bracing Between Framing Columns 3N & 4N (Similar between 3O and 4O)

Assumptions : Fy = 50ksi Fu = 65ksi (Typical L shape is A36)

Level 1 to Level 2 - Using same design for L2 to L3 and L3 to L4.

Designed bracing to resist “tension only” due to Wind loads, Row N resists 50% of the East/West wind load and row O resists 50% of the load. Each bracing will not support any gravity loads. Assume that the East/West wind produces 40 psf.

East or West Building Area - from mid height on Level 1 to Level 6
Area between column rows * 3 plus 1 ft each side of columns rows times 3 ½ floors + 3 ft parapet. Add this to the area of Level 6. Multiply all of this by the force

[(3 * 24) + 2] * [(3.5 * 14 )+ 3] + 13 (24 +2)
= [(74) * (52)] + [13 * 26] = 3848 + 338 = 4186 ft2 * 40 #/ft2 = 167440 or 167.4 k

Each row of columns N and O will withstand ½ of the wind 167.4 / 2 = 83.7 k

Length of the diagonal = √(332 + 142) = √1285 = 35.85 ft

Each diagonal tension force = ratio * force = 35.85'/33' * 83.7 k = 90.9 k (t)

Gross section yielding

Pn = Fy x Ag

LRFD Φt=0.90 & Load = 1.6W	ASD Ωt=1.67 & Load = 1.0W
Load = Φt * Pn = Φt * Fy x Ag	Load = Pn/ Ωt = Fy * Ag/Ωt
Ag = Load/ Φt * Fy	Ag = Load * Ωt / Fy
Ag = 90.9 k * 1.6 /(0.9 * 50ksi)	Ag = 90.9 k * 1.67/50ksi
Ag = 145.44 k /45 ksi = 3.23 in2	Ag = 151.8/50ksi = 3.04in2

Tensile rupture strength

Pn = Fu * Ae

LRFD Φt=0.75	ASD Ωt=2.00
Load = Φt * Pn = Φt * Fu * Ae	Load = Pn/ Ωt = Fu * Ae/ Ωt
Ae = Load/Φt * Fu	Ae= Load * Ωt /Fu
Ae = 90.9 k /0.75 * 65ksi	Ae= 90.9 k * 2/65ksi
Ae = 90.9 k /48.75ksi = 1.86in2	Ae= 181.8k /65ksi = 2.80in2

rx,y minimum= L/300	rx,y minimum= L/300
rx,y= 35.85 ft * 12 in/ft/300	rx,y = 430.2/300 = 1.434

Try L shape bracing:
L6x6x3/8	Wt. 14.9 #/ft	Ag = 4.38 in2	r = 1.87 in

For ¾” A325-N bolts	LRFD Capacity 15.9 k/bolt	ASD Capacity 10.6 k/bolt

LRFD	ASD
Diagonal Force/bolt Capacity 145.44 k /15.9 k = 9.1 bolts 90.9 k / 10.6 k = 8.6 bolts
Use two lines of 5 bolts
Table D3.1 AISC Case 8 Single angle with more than 4 fasteners per line use U = 0.80

Ae = U * An = 0.8 [4.38 in2 – 2(3/8”) (3/4” + 1/8”)] = 0.8 [4.38 – 0.656] = 0.8 * 3.723 = 2.98 in2
This Ae meets the Tensile Rupture Strength requirements calculated with ASD.

Level 4 to Level 5 - Both tension and compression.

Designed bracing to resist “both tension and compression” due to Wind loads, Row N resists 50% of the East/West wind load and row O resists 50% of the load. Each bracing will not support any gravity loads. Assume that the East/West wind produces 40 psf.

East or West Building Area - from mid height on Level 4 to Level 6

[(3 * 24) + 2] * (16/2 +3) + 13 (24 +2)
= [(74) * (11)] + [13 * 26] = 814 + 338 = 1152 ft2 * 40 #/ft2 = 46080 or 46.1 k

Each row of columns N and O will withstand ½ of the wind 46.1 / 2 = 23.1 k

Length of the diagonal = √(332 + 142) = √1285 = 35.85 ft

Each diagonal force = ratio * force = 35.85'/33' * 23.1 k = 25.1 k (t & c)

KL/r = 200	r = KL/200	r =