1. Define:

Newton	Btu

Cv	Specific Volume & units

Relationship Cp & Cv

lbf	Cp

Quality of two-phase mixtures	Enthalpy & units

Thermodynamic Zeroth Law	Thermodynamic First Law

Qualitatively plot a P-T phase diagram for a substance that expands on freezing and identify the melting, vaporization and sublimation lines, & the critical and triple points.

Describe the characteristic of each of the following processes:
(a) Pvn = constant	(b) n=1 © n=0	(d) n= infinity
(e) n=k=Cp/Cv	Plot b, c, d, e, on a P-v diagram

What is the ideal gas model?

What are the assumptions for ideal gas model? What are the effect of high pressure, low pressure, high temperature and low temperature on the model?

Fill in the blanks for the blank places in the steam table provided. Use all your thermodynamic relations to fill-up. Show all the calculations in the space provided.

Temp / (C)	Saturation Pressure (kPa)	Vf / m3/lg	Vg / m3/lg	uf / kJ/kg	ug / kJ/kg	hf / kJ/kg	hg / kJ/kg
85	57.83	0.00103	2.8280	355.84	2488.4	355.9
90	70.14	0.00104	2.3610		2494.5	376.92	2660.1
95	84.55		1.9820	397.88	2500.6	397.96	2668.1
100	101.35	0.00104	1.6729	418.94	2506.5		2676.1
105	120.82	0.00105	1.4194	440.02	2512.4	440.15
110	143.27	0.00105		461.14	2518.1	461.3	2691.5

Derive the general equation of the work performed in a closed system via the process, Pvn = constant, for n=1 and n=1.4 respectively. Show the area that is represented by the work in the P-v diagram.

Derive the general equation of the work performed in a closed system via the process, Pvn = constant, for n=1 and n=1.4 respectively. Show the area that is represented by the work in the P-v diagram.

Open book

A system consists of 0.9 kg of water undergoes a three-process cycle. Determine the net work and net heat transfer for each process and the entire cycle, in kJ. Neglect KE and PE. Qualitatively plot this cycle on a P-v diagram including the vapor dome.

1-2	Adiabatic compression from 1.4 Mpa, 90% quality to 4 Mpa and 550K
2-3	Isothermal process with W=500 kJ to P3 = 1.4 MPa
3-1	Isobaric process

A system consists of 2 kg of water undergoes a three-process cycle. Determine the net work and net heat transfer for each process and the entire cycle in kJ. Neglect KE and PE. Qualitatively plot this cycle on a P-v diagram including the vapor dome.

1-2	Adiabatic compression from 2 Mpa, 90% quality to 5 Mpa and 700K
2-3	Isothermal process with W=1000 kJ to P3 = 2 MPa
3-1	Isobaric process